Cleaning and disinfecting your water storage tank is necessary to protect you and your family’s health. Regular cleaning also makes water look and taste better. It is the owner’s responsibility to make sure that the water tank is cleaned and disinfected on a regular basis.

How Do I Know That Water Storage Tank Needs Cleaning?

The water from the delivery truck or pipe has been treated and is safe. If your water comes out of the tap looking a little cloudy of if water in your glass does not clear up after 1 minute, the sediment on the bottom of a storage tank could be the cause. It is often a sign that your tank needs cleaning.

How Often Water Storage Tanks Should Be Cleaned?

Water Storage tanks should be cleaned and disinfected a minimum of once a year. W

here the water supply has high levels of sediments at certain times of the year, cleaning more often is recommended.  If your water tastes, looks or smells unusual - the tank needs cleaning.

How To Clean Your Water Storage Tank?

1.	Shut off the valve to the water lines. Drain all water from the tank. If you have a 			non accessible tank proceed directly to Step 5, otherwise continue to Step 2.

2.	Wash and remove dirt from inside surfaces of tank by means of a high pressure hose or clean with a disinfected mop.

3.	Remove wash water by draining the wash water and sediment from the bottom of the 		tank. DO NOT ENTER THE TANK

4.	Rinse the inside surfaces of the water tank with clean drinking water. Again

remove wash/rinse water.

5.	Disinfect the inside surfaces of the tank and household distribution lines as follows:

a) 	Fill the tank with clean drinking water

b)	Add 5 ml of liquid household bleach for every liter of water the tank 				holds. 	For example, a 1000L tank will require 5 L of bleach.

c)	Open the valve to the distribution lines.

6.	Run water out of all water taps and faucets in the water lines, until the smell of chlorine is detected in the water.